## Slide 1: Gears & Levers
[Gear] noun
A toothed wheel that works with others to alter the relation between the speed of a driving mechanism and the speed of the driven part.
[Lever] noun
A rigid bar resting on a pivot (or fulcrum), used to move heavy or firmly fixed load with one end when a force is applied to the other
Unrestricted
LOAD

## Slide 2: Gears & Levers
Learning Aims | 
Knowledge | Skills
How levers work How gears work How teeth-count affects gear-wheel movement The principle of force magnifiers and distance magnifiers Understand Torque | Develop a simple mathematical rule Ratio and proportionality Application of gears and levers Explain engineering concepts using descriptions and mathematics

## Slide 3: Levers
Levers are one of the most basic and fundamental tools used by humans since the dawn of time.
The first written account of a lever was over 2,300 years ago and attributed to Archimedes;
“Give me a lever long enough and a fulcrum
on which to place it, and I shall move the World”.

## Slide 4
Class 1 lever
The fulcrum (pivot point) is between the load and force.
The nearer the fulcrum is to the load the less force is needed to move it.
LOAD
Class 2 lever
The load and the force are on the same side of the of the fulcrum.
The nearer the load is to the fulcrum the less force is needed to move it.
LOAD
LOAD
Class 3 lever
The force is acting between the fulcrum and the load.
Unlike class 1 and class 2 levers a class 3 lever delivers no Mechanical Advantage
Three classes of Lever
Notes: There are three classes of Levers.
<Click 1>
Class 1 lever. The fulcrum (or pivot point) is between the load and the force (the input force and the output force). The nearer the fulcrum is to the load the less input force is required to move it, this gives a Mechanical Advantage.
<Click 2>
Class 2 lever. The load and the input force are on the same side of the fulcrum. Again, the nearer the load is to the fulcrum the less force is required to move it.
<Click 3>
Class 3 lever. The force is between the fulcrum and the load. Unlike Class 1 and Class 2 levers the Class 3 lever does not provide an Mehcanical advantage

## Slide 5
Class 1 lever
The fulcrum (pivot point) is between the load and force.
The nearer the fulcrum is to the load the less force is needed to move it.
LOAD
Examples of class 1 Lever
Input
Force
Output
Force
Fulcrum
Fulcrum
Notes: This slide shows examples of a Class 1 lever
A seesaw and a pair of scissors.

## Slide 6
Class 2 lever
The load and the force are on the same side of the of the fulcrum.
The nearer the load is to the fulcrum the less force is needed to move it.
LOAD
Input
Force
Output
Force
LOAD
Fulcrum
Input
Force
Examples of class 2 Lever
Notes: This slide shows examples of a Class 2 lever
A wheelbarrow and a nutcracker.

## Slide 7
LOAD
Class 3 lever
The force is acting between the fulcrum and the load.
Unlike class 1 and class 2 levers a class 3 lever delivers no Mechanical Advantage
Fulcrum
Input
Force
Output
Force
Fulcrum
Input
Force
Input
Force
Output
Force
Output
Force
Examples of class 3 Lever
Notes: This slide show examples of a class 3 lever.
A stapler and a pair of tweezers.

## Slide 8
LOAD
Class 3 lever
The force is acting between the fulcrum and the load.
Unlike class 1 and class 2 levers a class 3 lever delivers no Mechanical Advantage
Examples of class 3 Lever
1
1
1
2
2
2
2
Notes: Tis is an optional slide.
The nail clippers shown use two class 3 levers.

## Slide 9
Mechanical Advantage =
Load
Effort
500N
100N
= 5
Velocity Ratio =
distance moved by effort
distance moved by load
d1
d2
LOAD
Effort
LOAD
Effort
LOAD
Effort
d2
d1
100N
500N
LOAD
Effort
L1
L2
Mechanical Advantage =
L2
L1
Notes: A lever is a basic mechanism that produces Mechanical Advantage. The advantage is that the output Force is greater than the input Force.
Mechanical Advantage (MA) is a ratio and as such (for levers) can be calculated using either Load (weight, or output force) divided by effort (input force), or length of input arm (L2) divided by the length of the output arm (L1)
This Mechanical Advantage does not come free. The Velocity Ratio shows the distance moved by the effort (the input Force) is greater than the distance moved by the Load (output Force).
<Click 1>

## Slide 10
LOAD
Effort
F
W
L1
L2
Calculating the force required for equilibrium
F x L2 = W x L1
(W x L1)
L2
F =
100kg
W
250mm
700mm
F
1kg
100mm
250mm
F
25kg
15mm
425mm
Notes: When a lever (or beam) is in equilibrium it is “balanced”, i.e. the input equals the output.
<Click 1>
The equation to calculate the force required for equilibrium is “input force or effort (F) multiplied by the length of the input arm = the weight or output force (W) multiplied by the length of the output arm: F x L2 – W x L1”
<Click 2>
To calculate the Force (or effort) required to balance a lever with a specified output the equation is F = (W x L1) divided by L2
<Click 3>
Using this formula calculate the Force required to achieve equilibrium in the following levers (beams).
Note to teacher: you can also ask the students to calculate the Mechanical Advantage of each lever
<Click 4>
See if you can rearrange the formula to calculate the load (or output) would be for the following lever with an input load (force) of 100kg.

## Slide 11
100kg
W
250mm
700mm
F
1kg
100mm
250mm
F
25kg
15mm
425mm
(1kg x 100mm)
250mm
F =
F = 0.4kg
(25kg x 15mm)
425mm
F =
F = 0.882kg
F x L2 = W x L1
(F x L2)
L1
W =
(100kg x 700mm)
250mm
W =
W = 280kg
Mechanical Advantage
L2
L1
250mm
100mm
= 0.25
MA =
L2
L1
425mm
15mm
= 28.3
MA =
Notes: <Click 1>
In the first example the load is 1kg. To calculate for Force (load) required to achieve equilibrium we use the equation
<Click 2>
Which gives a Force of <Click 3> 0.4kg
To calculate Mechanical Advantage
<Click 4>
<Click 5>
In the second example the load is 25kg. To calculate the Force (load) required to achieve equilibrium the equation is;
<Click 6>
Giving an answer of <Click 7> 0.882kg
Note that due to the position of the Fulcrum (near to the output) and the distance at which the input Force is applied the input Force required to achieve equilibrium is relatively small.
<Click 8>
Mechanical Advantage for the second lever example is calculated using;
<Click 9>
In this example we know the input Force but not the output Force or weight. This requires the formula to be re-ordered to solve for W <Click 10>

## Slide 12
1kg
F
100mm
350mm
W
F
L1
L2
Calculating the force required for equilibrium
F x L2 = W x L1
(W x L1)
L2
F =
(1kg x 100mm)
350mm
F =
F = 0.285kg
Notes: Optional slide.
In this example the lever is a class 2 lever with the fulcrum at one end of the lever (beam) and the load positioned between the fulcrum and the input Force. Obviously the input Force is required to act in the opposite direction, but the equation is still the same.
Students can be asked to convert the input force and output Forces into Newtons;
1 Newton = weight (kg) x 9.81 (m/s)

## Slide 13: Gears
A toothed wheel that works with others to alter the relation between the speed of a driving mechanism and the speed of the driven part.

## Slide 14
Types of gears and terminology
Pinion gear: this is a round gear and usually the smallest gear in a drive chain.
Pinion
Pinion
Rack
Rack & Pinion:
this mechanism changes rotary movement into linear movement.
Worm gear: are used when large gear reductions are needed. The worm gear can easily turn the gear but the gear cannot turn the worm.
Worm gear

## Slide 15
Types of gears and terminology
Spur gears: operate on axes which are parallel.
Bevel gears: are gears where the axis of rotation is at an angle and are commonly used to change the axis of rotation in a gear-train.
Gear-train: a mechanical system consisting of two or more intermeshing gears.

## Slide 16
Gear ratio: is the input speed relative to the output speed.
Types of gears and terminology
60 teeth
15 teeth
If the smaller gear is the driver (input)
Gear ratio =
If you know the input speed you can calculate the output speed.
input speed
gear ratio
output speed =
Input speed 200 rpm
number of teeth on output gear
number of teeth on input gear
60
15
=
4
200
4
=
50 rpm
Gear ratio typically displayed as 4 : 1
This means the driver gear (input) rotates four times to make the driven gear (output) rotate once.

## Slide 17
Gear A to Gear B
8 : 24 teeth
1 : 3 ratio
Three turns of A = 1 turn of B
Gear B has 3x the turning force as Gear A
Intermeshing gears turn in opposite directions
Gear B to Gear C
24 : 16 teeth
3 : 2 ratio
10cm 30cm
Gears can also be considered as levers -
1/3 of the distance moved results in 3 times the force
Gear B can be considered as an idler gear. The work is transferred from gear A to gear C but the idler gear B makes gear C turn in the same direction as gear A
Gear A to Gear C
8 : 16 teeth
1 : 2 ratio
A
B
C
Click to start wheels, then step back for summary
Notes: This slide automatically builds. Show in Presentation Mode.
<Click 1> to start the animation of the gears. The text will appear at timed intervals over the course of about 1 minute and summarises the core concepts the students should have been able to discover and teach each other

## Slide 18
50 teeth
25 teeth
Input speed 1000 rpm
140 teeth
60 teeth
Input speed 150 rpm
Gear ratio =
number of teeth on output gear
number of teeth on input gear
50
25
=
1 : 2
Gear ratio =
input speed
gear ratio
output speed =
1000
2
=
500 rpm
output speed =
140
60
=
1 : 2.333
Gear ratio =
150 2.333
=
64.28 rpm
output speed =
Notes: Leave the slide and ask students to calculate the Gear Ratio and output speed of the two examples.
<Click 1> to reveal the Gear Ratio for example 1
<Click 2> to reveal the output speed for example 1
<Click 3>to reveal the Gear Ratio for example 2
<Click 4> to reveal the output speed for example 2

## Slide 19: Torque
Torque is the turning (rotational) force on an object such as a bolt, or wheel (or gear).
The symbol for Torque is the Greek letter Tau (τ)
Torque is measured in Nm
τ = r x F
Distance (r)
Force (F)
Torque

## Slide 20
Torque
Force
Door
A
Force
Door
B
Force
Door
C
Notes: Assume you’re trying to open a door. Above there are three different scenarios.
In scenario A; if you push close to the hinge it is possible to open the door but a greater force is required
In scenario B: if you push in the middle of the door less force is required to open it.
In scenario C: pushing the door at a point furthest away from the hinge is much easier, requiring the least amount of force in the three scenarios.

## Slide 21
Force
θ = 90°
lever arm r
Force
θ
lever arm r
Force
θ
lever arm r
Maximum torque is produced when θ is 90°
τ = r F sinθ

## Slide 22
Levers
Discover how your system works
Can you product a Force Multiplier? Something where for a smaller input force you can produce a larger output force.
Levers
Discover how your system works
Can you product a Distance Multiplier? Something where for a smaller movement you can produce a larger movement.
Gears
Discover how your system works
Can you product a Force Multiplier? Something where for a smaller input force you can produce a larger output force.
Gears
Discover how your system works
Can you product a Distance Multiplier? Something where for a smaller movement you can produce a larger movement.
Classroom Task
LOAD